## Slide 1
CPCCCM2006
Apply basic levelling procedures
Release 1 · CPC Construction, Plumbing and Services Training Package · Sample RTO

## Slide 2
CPCCCM2006 · About this unit (1/2)
About this unit
Apply basic levelling procedures
This unit of competency specifies the outcomes required to carry out levelling in a single plane for the purpose of establishing correct and accurate set-out of building components. It includes the set-up, testing and use of levelling devices, and establishing and transferring heights using a range of levelling equipment. The unit supports workers in the construction industry who use a variety of common methods and equipment when working with others and as

## Slide 3
CPCCCM2006 · About this unit (2/2)
About this unit
Apply basic levelling procedures
a member of a team. It applies to levelling work on residential and commercial work sites. No licensing, legislative, regulatory, or certification requirements apply to this unit of competency at the time of endorsement.

## Slide 4
CPCCCM2006 · Element 1
Element 1
Plan and prepare
5 performance criteria
Element 1 is done properly when the crew is standing at the datum with a confirmed level schedule in the field book, a signed SWMS that covers the hazards actually present, hazards reported in writing, every piece of levelling gear checked and serviceable with any fault tagged out, and roles and hand signals agreed and demonstrated — so nothing but the levelling itself is left to work out.
Notes: For the trainer: · Students routinely skip the datum. Give them a plan with two possible benchmarks marked and watch how many just start shooting from the nearest peg. Make them nominate the datum out loud and justify it before they touch the instrument. · Watch for 'confirming' that is really just receiving. The student should be repeating figures back — 'datum peg at the driveway, RL 100.000, finished floor 100.150, that's 150 up' — and getting a yes. · Offsets and gradients trip people up. Have them do the arithmetic on paper at the pre-start, not in their head at the staff. A 1:100 fall over 12 m is 120 mm and half the group will say 12 mm. · Overhead powerlines are the safety callout for this unit. Reinforce that a telescopic staff is a conductor and that the exclusion zone applies to the staff, not the person. Ban extending staffs under or near lines, full stop. · Common site-walk failure: students look at the ground and never look up or behind them. Send them out with a checklist that forces eyes up, eyes down, eyes along the sight line. · Students report hazards verbally and think that is finished. Insist on the written step as well — pre-start book, hazard report, or whatever the RTO's simulated site procedure requires — and mark it as incomplete if the paperwork is missing. · Equipment checks get done as a glance. Make them handle it: pick the tripod up by the head and feel for movement, rotate the instrument through 360 degrees to see the bubble stay centred, extend and lock every staff section, run the water hose out and look for air. · Expect students to find a fault and keep going because they do not want to lose time. Plant a deliberate fault — a loose leg clamp, a flat laser battery, a staff clip that will not lock — and assess what they do about it. · Hand signals are treated as a joke until the first time someone shouts across a slab for five minutes. Make signals agreed and demonstrated before they separate, and hold students to the agreed set even when they could hear each other. · Watch PPE at the pre-start, not just on the tools. Sun protection matters — levelling crews stand in the open for hours — and it is a legitimate part of planning on an Australian site.

## Slide 5
CPCCCM2006 · Element 1 — what you need (1/3)
What you need (1/3)
Element 1 — Plan and prepare
Set-out plan, footing detail and RL or levels schedule for the job (current revision)
SWMS or JSA for basic levelling procedures, plus the site safety plan
Site hazard report form and pre-start/toolbox record
Field book or booking sheet and a pen (not a pencil for records)
Automatic (dumpy) level in its case, with tripod
Telescopic 5 m E-face levelling staff with staff bubble
1200 mm aluminium spirit level and 3 m straight edge
Clear water level hose (minimum 15 m), filled and free of air

## Slide 6
CPCCCM2006 · Element 1 — what you need (2/3)
What you need (2/3)
Element 1 — Plan and prepare
Rotating laser level with tripod, receiver/detector and staff clamp
Spare batteries for laser and detector
8 m tape measure and 30 m fibreglass tape
Timber pegs, hardwood profiles, club hammer, string line and chalk line
Permanent marker, lumber crayon and spray marking paint
Equipment serviceability checklist and out-of-service tags
Lint-free cloth and lens brush for instrument optics
Two-way radios (as a backup to hand signals, not a replacement)

## Slide 7
CPCCCM2006 · Element 1 — what you need (3/3)
What you need (3/3)
Element 1 — Plan and prepare
Hard hat, hi-vis vest or shirt, steel-capped safety boots, safety glasses, work gloves
Broad-brim hat attachment, sunscreen and drinking water for extended outdoor work

## Slide 8
CPCCCM2006 · Element 1 — 1. Why planning decides the accuracy
Why planning decides the accuracy
Element 1 — Plan and prepare
Wrong datum repeats through every mark you make that day
Errors are found at fit-out, not at set-out — after the concrete
A loose tripod clamp beats a bad instrument for causing bad levels
Half an hour of planning saves a day of demolition
Notes: Levelling work goes wrong long before anyone looks through an instrument. It goes wrong when the datum was never confirmed, when the staff man and the instrument man never agreed on what a raised arm means, or when a tripod with a loose leg clamp gets carried out to a windy slab. Element 1 is the half hour of work that makes the rest of the day accurate. You get the job requirements in your hands, you walk the ground you are about to work on, you confirm the safety controls that apply to standing in the open with a metal staff, and you check that every piece of gear you are about to trust is actually serviceable. Start with the paperwork. On a house slab that might be a set-out plan and a footing detail; on a commercial job it might be a survey mark schedule, an RL sheet and a levels drawing. You are looking for one thing above all others — where the datum is and what its reduced level (RL) is — and then the finished levels you have to transfer off it: floor level, top of footing, invert of a drain, top of a retaining wall. Read the legend and the notes, not just the numbers. If a level is shown as an offset from the datum rather than an RL, work out the figure before you leave the shed and write it down. Then confirm it with the person who owns the job — the supervisor, leading hand, site engineer or builder. Confirming means saying the numbers back and getting agreement, not nodding at a drawing. A misread datum repeats itself through every mark you make and it is not found until something does not fit. Then walk the site. You are looking at the ground you will set the tripod on, the sight lines between the instrument and every point you have to shoot, and what is above you. Overhead powerlines and an extended 5 m staff are the classic killer in this trade — an aluminium staff does not need to touch a line to arc. Look also for open excavations and trench edges, unbattered faces, plant movement and reversing routes, soft or filled ground that will let a tripod settle, traffic, and heat, glare and wind that will affect both you and the readings. Identify hazards within your own role, control what you are authorised to control, and report the rest through your workplace procedure — verbally to the supervisor and on the hazard report or in the pre-start book. Confirm the SWMS or JSA for the levelling task covers what you found, sign on to it, and check your equipment last: tripod legs and clamps, the compensator in an automatic level, bubble vials, battery and detector on a laser, staff sections and locking clips, hoses free of kinks and air. Anything unserviceable is either fixed on the spot or tagged out and reported — never "it'll do". Finish by agreeing with your offsider who is on the instrument, who is on the staff, who records, and the hand signals you will use when you are 60 m apart and cannot hear each other over a rock breaker.

## Slide 9
CPCCCM2006 · Element 1 — 2. Reading the job — what you are looking for
Reading the job — what you are looking for
Element 1 — Plan and prepare
The datum or TBM and its RL — find it on the plan and in the ground
Every required height: FFL, top of footing, invert level, top of wall
Falls and gradients converted to millimetres before you start
Legend, notes and revision date — not just the numbers
Write the level schedule in the field book

## Slide 10
CPCCCM2006 · Element 1 — 3. Confirming with the supervisor
Confirming with the supervisor
Element 1 — Plan and prepare
Read the figures back out loud and wait for a yes
A nod at a drawing is not confirmation
Write down any verbal change: figure, date, who gave it
Plan and supervisor disagree? Stop and resolve it in writing

## Slide 11
CPCCCM2006 · Element 1 — 4. Site walk — eyes up, down and along
Site walk — eyes up, down and along
Element 1 — Plan and prepare
UP: powerlines, service drops, crane and excavator swing
DOWN: excavations, edges, starter bars, soft or filled ground
ALONG: sight lines blocked by stacks, fences, formwork
AROUND: plant routes, other trades, traffic
WEATHER: glare, heat shimmer, wind, low sun

## Slide 12
CPCCCM2006 · Element 1 — 5. The killer hazard — overhead powerlines
The killer hazard — overhead powerlines
Element 1 — Plan and prepare
A telescopic staff conducts — aluminium and fibreglass both
Electricity arcs; the staff does not have to touch the line
Exclusion zone applies to the staff, not just the person
Never extend a staff to find out how close it is
Point inside the zone? Report it and use another set-up

## Slide 13
CPCCCM2006 · Element 1 — 6. Reporting hazards
Reporting hazards
Element 1 — Plan and prepare
Control what is inside your role
Report the rest to the supervisor — verbally, then in writing
Hazard report, pre-start book or site diary: dated and named
Immediately dangerous means stop now, not at smoko
Check the SWMS actually covers what you found, then sign on

## Slide 14
CPCCCM2006 · Element 1 — 7. Serviceability checks before the job starts
Serviceability checks before the job starts
Element 1 — Plan and prepare
Tripod first: lift by the head, feel for play, tighten every clamp
Level: clean optics, bubble stays centred through 360 degrees
Tap the instrument — the compensator must swing free
Staff: every section extends and locks, face readable
Spirit level: reverse it end-for-end — same reading or it's out
Water level: no air, no kinks. Laser: battery, self-level, detector

## Slide 15
CPCCCM2006 · Element 1 — 8. Faults, roles and signals
Faults, roles and signals
Element 1 — Plan and prepare
Fix what you're authorised to fix — batteries, cleaning, clamps
Everything else: out-of-service tag and a written report
Never work around a known fault
Agree roles: instrument, staff, recorder, spotter
Agree signals: left, right, raise, lower, hold, read, STOP
Demonstrate every signal before you separate

## Slide 16
CPCCCM2006 · Performance criterion 1.1
1.1
Job requirements are obtained, confirmed with relevant personnel, and applied to planning.

## Slide 17
CPCCCM2006 · Performance criterion 1.2
1.2
Work site is inspected, and conditions and hazards are identified within scope of own role and reported according to workplace procedures.

## Slide 18
CPCCCM2006 · Performance criterion 1.3
1.3
Health and safety requirements for levelling procedures are confirmed and applied to planning.

## Slide 19
CPCCCM2006 · Performance criterion 1.4
1.4
Levelling tools and equipment are selected according to job requirements, checked for serviceability, and faults are rectified or reported before starting work.

## Slide 20
CPCCCM2006 · Performance criterion 1.5
1.5
Team roles and verbal and non-verbal communication signals are confirmed, as required.

## Slide 21
CPCCCM2006 · Element 1 — activities (1/3)
Activities (1/3)
Element 1
Practical — Datum hunt and level schedule (60 min): You are given a residential set-out plan and footing detail for a single-storey slab-on-ground job. Working in pairs, identify the datum shown on the plan and its RL, then list every level you would have to transfer for the footings and slab. Where a level is shown as a fall, a gradient or an offset, work out the finished figure in millimetres and show your working. Write the lot up as a level schedule in your field book. When you are done, present the schedule to your trainer acting as the site supervisor and confirm the figures by reading them back. Your trainer will change one figure verbally — record the change and note who gave it and when.
Practical — Pre-start site walk and hazard report (45 min): Walk the training compound or simulated work site with your partner as if you were about to set up a level and transfer heights across it. Identify hazards that affect levelling work specifically: overhead services, excavations and edges, plant and traffic movement, soft or filled ground under the tripod, obstructed sight lines, glare, wind and heat. For each one, state whether it is inside your role to control, and what you did or who you told. Complete the site hazard report form and hand it in. Then read the SWMS provided for the levelling task and mark any hazard you found that the SWMS does not cover.

## Slide 22
CPCCCM2006 · Element 1 — activities (2/3)
Activities (2/3)
Element 1
Practical — Serviceability check of levelling equipment (60 min): At the equipment bench you will find an automatic level and tripod, a telescopic staff, a 1200 mm spirit level with a straight edge, a clear water level hose, and a rotating laser with detector. Work through each item against the manufacturer's instructions and a serviceability checklist: tripod legs, clamps and shoes; instrument case, footscrews, bubble vial and compensator; staff sections, locking clips and face; spirit level vial reversed end-for-end on a known flat surface; hose free of air and kinks; laser battery, self-levelling function and detector. At least one item on the bench has a fault. Record every check, state which item is unserviceable, and take the correct action — rectify it if you are authorised and able to, otherwise tag it out and report it, in writing, t…
Practical — Roles and signals brief (30 min): In a team of three, run a two-minute pre-start brief before a levelling task. Nominate who is on the instrument, who is on the staff and who records. Agree and demonstrate hand signals for: move left, move right, raise the staff, lower the staff, hold steady, reading taken, stop work. Then separate to at least 50 m and complete a short set of instructions given by signal only, with no shouting and no phones. Swap roles and repeat.

## Slide 23
CPCCCM2006 · Element 1 — activities (3/3)
Activities (3/3)
Element 1
Quiz — Planning a levelling job — short answer (30 min): Ten short-answer questions set on a real job: reading an RL off a plan, working out a fall in millimetres, deciding whether a hazard is yours to control or to report, choosing the right levelling device for a job described in the question, and stating what you do with a level that will not hold its bubble. Closed book except for the plan extract provided.

## Slide 24
CPCCCM2006 · Element 2
Element 2
Set up and use levelling device
4 performance criteria
When this element is done properly you are looking at every required height from the work instructions marked on site with a fine labelled line, each one proven from two instrument positions and closed back to the datum inside the job tolerance, with a completed and signed booking sheet showing the readings, the reduced levels, the arithmetic check, the closing error and the tolerance check on the instrument you used.
Notes: For the trainer: · Most errors are not instrument errors. Watch for the staff off plumb, the staff foot on soft fill or a loose stone, and the staff extended but not clicked into the locked position — all read high or low and all look fine from the instrument. · Students routinely centre the bubble, then knock a tripod leg with their boot while walking to the eyepiece. Teach them to check the bubble again immediately before each reading, not just at set-up. · Parallax is invisible to a beginner. Make each student move their head up and down at the eyepiece and watch the crosshair swim against the staff, then fix it with the eyepiece focus. Until they have seen it, they will not believe it matters. · The two peg test defeats students because they lose track of which pair of readings is which. Insist on a sketch with A and B labelled and both instrument positions drawn before any reading is taken. · Expect confusion between 'the level is out of tolerance' and 'I made a mistake'. Have them repeat the test before condemning the instrument, and require a report to the supervisor plus an out-of-service tag if it fails twice — not a quiet adjustment in the shed. · Watch for students adding when they should subtract. Rise and fall trips people up; drill the sentence 'bigger reading means lower ground' until it is automatic. · Reinforce that a reading called across a site must be repeated back. On a windy or noisy site, agreed hand signals do the work — set them and use them, do not improvise. · Safety callouts: never set up a tripod or extend a staff under or near live overhead powerlines; a 5 m aluminium staff is a conductor. Keep tripod legs out of walkways and traffic paths, or cone them off. Never look at the sun through the telescope. Watch for hose across access ways with the water level method. · Laser levels need eye protection discipline — no staring into the beam, and the class rule is beam off when the instrument is being carried or repositioned. · Booking sheets are where students go thin. Do not accept loose numbers on a scrap of plasterboard. Require the sheet to be legible, dated, signed, with the arithmetic check completed and the closing error stated. · Students often mark a height with a fat carpenter's pencil blob 6 mm wide and call it 3 mm accuracy. Make them justify their mark against the tolerance in the job spec.

## Slide 25
CPCCCM2006 · Element 2 — what you need (1/3)
What you need (1/3)
Element 2 — Set up and use levelling device
Automatic (dumpy) or optical level with its carry case and manufacturer's manual
Heavy-duty aluminium tripod with adjustable legs and fixing screw
5 m telescopic E-face levelling staff with staff bubble
1200 mm box-section spirit level and 3 m aluminium straight edge
Rotating laser level with tripod, laser detector and clamp, and its manual
20 m clear water level hose with end fittings, plus clean water
Timber pegs (50 x 50) and a claw hammer or peg driver

## Slide 26
CPCCCM2006 · Element 2 — what you need (2/3)
What you need (2/3)
Element 2 — Set up and use levelling device
Stringline and line blocks
8 m tape measure and a 30 m fibreglass tape
Carpenter's pencil, fine 0.5 mm mechanical pencil, marking crayon and permanent marker
Nails or marker blocks for marking on surfaces that will not hold a pencil line
Level book or organisational levelling booking sheet, clipboard and calculator
Job set-out sheet, slab and footing plan and the site datum details
SWMS for levelling work and the site safety plan

## Slide 27
CPCCCM2006 · Element 2 — what you need (3/3)
What you need (3/3)
Element 2 — Set up and use levelling device
Hard hat, hi-vis long-sleeve shirt, safety boots, safety glasses, gloves, sunscreen
Traffic cones or barrier mesh to protect the tripod set-up

## Slide 28
CPCCCM2006 · Element 2 — 1. What Element 2 delivers
What Element 2 delivers
Element 2 — Set up and use levelling device
Heights from the drawings, marked on site, that other trades build to
Every height is a difference from one datum
Datum may be a survey peg, PSM, kerb invert or site TBM
Wrong by 5 mm at the instrument means wrong by 5 mm everywhere
Nothing on site tells you it is wrong until it is concreted
Notes: Element 2 is where the levelling actually happens. You start with a set of work instructions — a slab plan, a set-out sheet, a footing detail — and a datum on site, and you finish with marks on pegs, profiles, formwork or walls that everyone else on the job builds to. The datum might be a survey peg, a permanent survey mark, a kerb invert, a bolt in a driveway or a temporary bench mark (TBM) your supervisor has established. Whatever it is, every height you shoot is a height above or below that one point, so the first job is always to work out from the drawings what heights are required, what they are measured from, and what the difference is in millimetres. Finished floor level 150 above natural surface does not mean anything until you have turned it into a reading on a staff. Once you know the numbers, you choose the device that suits the distance and the accuracy required, set it up so it is genuinely level, and prove it is reading true before you trust it. An automatic or optical level goes on a tripod with the legs firmly footed and the circular bubble centred, and you confirm it against manufacturer tolerance with a two peg test — typically the instrument must agree within about 3 mm over 30 m, but the manual is the authority, not the rule of thumb. A spirit level and straight edge is only as good as its own accuracy (commonly 0.5 mm per metre) and is checked by reversing it end for end on the same surface. A rotating laser is checked with its detector, not by eye. A water level has no calibration to check at all, but it is useless with an air bubble in the hose. Skipping the check is the single most expensive habit in levelling, because a level that is out by 5 mm is out by 5 mm on every single reading you take, and nothing on site tells you until the plumber finds the fall running the wrong way. Shooting levels is a two-person job done to an agreed set of signals. The staff holder keeps the staff plumb on a solid point and steady; the instrument operator focuses the crosshair, kills parallax, reads to the nearest millimetre and calls the reading back so it is confirmed before it is written. Heights are transferred by holding or driving the staff until the reading matches the figure you calculated, then marking the point clearly — a fine pencil or crayon line, an arrow to the exact line, and a label such as 'FFL' or '1000 ABOVE FFL' so nobody has to guess later. Then you prove it: move the instrument to a second position, re-read the marks, and close the loop back to your datum. Every reading, calculation and closing error goes on the booking sheet or in the level book while you are still standing there, with the arithmetic check done and the instrument, date and operator recorded. If it is not written down, it did not happen, and the next trade has nothing to work from.

## Slide 29
CPCCCM2006 · Element 2 — 2. Step 1 — read the job, do the sums
Step 1 — read the job, do the sums
Element 2 — Set up and use levelling device
Identify the datum before you touch any equipment
RL is an absolute height; '150 above NS' is an offset
Convert every required height to millimetres of rise or fall
Write the numbers down, then check them once more
No datum on site = stop and ask the supervisor

## Slide 30
CPCCCM2006 · Element 2 — 3. Choosing the device
Choosing the device
Element 2 — Set up and use levelling device
Spirit level + straight edge: short runs, typically 0.5 mm per metre
Water level: long runs, around corners, no line of sight needed
Automatic/optical level + staff: open site, millimetre reading
Rotating laser + detector: one operator, repetitive heights
Device accuracy must be finer than the job tolerance

## Slide 31
CPCCCM2006 · Element 2 — 4. Setting up an automatic level
Setting up an automatic level
Element 2 — Set up and use levelling device
Firm ground, legs spread wide and pressed in
Level the tripod head by leg length first
Then centre the circular bubble with the footscrews
Bubble must stay centred through a full rotation
Focus crosshair, then staff — kill the parallax
Never set up near overhead powerlines

## Slide 32
CPCCCM2006 · Element 2 — 5. Two peg test — prove it before you use it
Two peg test — prove it before you use it
Element 2 — Set up and use levelling device
Two firm pegs about 30 m apart, marked A and B
Read A and B from midway = the true difference
Read A and B from 2 m behind A = the test difference
Compare the two against the manual's tolerance
Fails twice = tag out of service and report it
Sketch both set-ups before you take a reading

## Slide 33
CPCCCM2006 · Element 2 — 6. Shooting and transferring
Shooting and transferring
Element 2 — Set up and use levelling device
Agree hand signals before you separate
Staff plumb, foot on a solid point, section locked out
Instrument height = datum RL + backsight
Required reading = instrument height − target RL
Read to the millimetre, call it, have it repeated back
Keep backsight and foresight distances roughly equal

## Slide 34
CPCCCM2006 · Element 2 — 7. Marking so the next trade can use it
Marking so the next trade can use it
Element 2 — Set up and use levelling device
One fine line, not a 6 mm pencil blob
Arrow pointing to the line
Label it: FFL, TOP OF FOOTING, 1000 ABOVE FFL
Nail or marker block where the surface won't take a line
Walk the marks with the supervisor before you pack up

## Slide 35
CPCCCM2006 · Element 2 — 8. Verify — two positions and close the loop
Verify — two positions and close the loop
Element 2 — Set up and use levelling device
Re-read the datum before finishing the run
Move the instrument and re-read every mark
Marks must agree from both positions within tolerance
Close back onto the datum and state the closing error
Error outside tolerance = re-run, do not fudge it

## Slide 36
CPCCCM2006 · Element 2 — 9. Records — if it isn't written, it didn't happen
Records — if it isn't written, it didn't happen
Element 2 — Set up and use levelling device
Book every reading as it is taken
Reduce by rise and fall or height of collimation
Arithmetic check: ΣBS − ΣFS = last RL − first RL
Record instrument ID, tolerance check, date, weather, names
Lodge the sheet with the supervisor or site records

## Slide 37
CPCCCM2006 · Element 2 — 10. Where it goes wrong
Where it goes wrong
Element 2 — Set up and use levelling device
Staff leaning off plumb — reads high
Tripod leg kicked after levelling up
Parallax not removed at the eyepiece
Metres and millimetres mixed in one calculation
Instrument never checked against the manual
Numbers on a scrap of plasterboard instead of the sheet

## Slide 38
CPCCCM2006 · Performance criterion 2.1
2.1
Required heights or levels are identified from work instructions.

## Slide 39
CPCCCM2006 · Performance criterion 2.2
2.2
Levelling device is set up, and levelling device tolerance is checked according to manufacturer specifications.

## Slide 40
CPCCCM2006 · Performance criterion 2.3
2.3
Levels are shot and heights are transferred to required location and marked according to job requirements.

## Slide 41
CPCCCM2006 · Performance criterion 2.4
2.4
Results of levelling activities are documented according to organisational requirements.

## Slide 42
CPCCCM2006 · Element 2 — activities (1/3)
Activities (1/3)
Element 2
Practical — Two peg test on an automatic level (60 min): Working in pairs, drive two pegs 30 m apart on a level area of the training compound. Set the tripod and automatic level midway between them, level up, and read the staff on peg A and peg B. Record both readings and calculate the true difference in height. Move the instrument to within about 2 m of peg A and repeat both readings. Calculate the second difference and compare the two results. Look up the permitted tolerance in the manufacturer's manual for the instrument you are using, state on your sheet whether the instrument passes or fails, and hand the completed sheet to your trainer. If it fails, repeat the test once, then tag the instrument and report it to your supervisor using the workshop fault report.

## Slide 43
CPCCCM2006 · Element 2 — activities (2/3)
Activities (2/3)
Element 2
Practical — Transfer heights with three devices (180 min): You will be given a set-out sheet showing a datum peg and three required heights: a footing top, a finished floor level, and a 1 m offset line on a wall frame. Transfer and mark all three heights three times over — once with an automatic/optical level and staff, once with a spirit level and straight edge, and once with either a water level or a rotating laser and detector. Use agreed hand signals with your partner and swap roles so each of you both reads the instrument and holds the staff. Mark every height with a fine line, an arrow and a written label. Then set the instrument up in a second position and re-check all three marks. Record every reading, calculation and the closing error on the booking sheet.
Practical — Book and reduce a levelling run (75 min): Run a series of levels from a given TBM around five points and back to the TBM. Book the readings in the field book using either the rise and fall or height of collimation method as directed. Reduce the levels, complete the arithmetic check, state the closing error in millimetres, and say whether the run is acceptable against the tolerance in the job specification. Record the instrument identification, date, weather, your name and your partner's name. Submit the field book pages.

## Slide 44
CPCCCM2006 · Element 2 — activities (3/3)
Activities (3/3)
Element 2
Written — Reading the job and doing the sums (45 min): You are given an extract of a slab and footing plan with a datum peg marked RL 24.500, a finished floor level shown as RL 24.900, and a footing invert 600 below FFL. Answer a short set of workplace questions: what staff reading on the datum tells you the instrument height, what reading you need on the footing invert, and what you would do if the point you need to mark is 40 m away and behind a shed. Show all calculations in millimetres.
Quiz — Devices, limits and checks (30 min): Twenty short questions on which device suits which job on site, working range and accuracy limits, how each device is proven before use, what a failed check means for the day's work, and what has to appear on a levelling record before it is handed over.
Verbal — Handover of levels to the next trade (15 min): Explain to your trainer, standing at your marks, what the marks mean, what datum they came from, which instrument you used, when it was last checked, what your closing error was, and where the record is filed. Answer questions on what you would do if the concreter told you the marks looked 10 mm out.

## Slide 45
CPCCCM2006 · Element 3
Element 3
Clean up
2 performance criteria
When this element is done properly you are looking at a work area with only the pegs and marks that are meant to still be there, each capped or flagged, no holes, no loose line, no offcuts, no bins with the wrong material in them, and the levelling gear back in store clean, dry, checked, cased the way the manual says, with the results recorded and anything faulty tagged out and reported.
Notes: For the trainer: · The single most expensive mistake in this element is pulling a datum peg. Set the job up so that at least one retained peg is present, and mark any student who clears it without asking as not yet competent for 3.1. Debrief it as a real cost: the whole set-out has to be re-run from the benchmark. · Watch for students who make one big pile in the middle of the slab and intend to sort it later. Sorting at the point of pick-up is the habit you want. Sorting later never happens. · Students routinely wipe an objective lens with a hi-vis sleeve, a rag with grit in it, or metho. Demonstrate the correct sequence once - blow or brush loose grit off, then a clean lens cloth - and then check each student's instrument under a torch for new swirl marks. · Damp storage is invisible on the day and fatal in three months. Make students open a case and physically feel the foam before the instrument goes in. If it is wet, the instrument stays out until both are dry. · Battery removal gets skipped because the laser is going out again tomorrow. Have a leaking or corroded battery compartment on hand to pass around - it makes the point faster than any explanation. · Star pickets are the sleeper hazard. Any picket that stays in the ground must be capped; any picket pulled must go on the stack, not lie in the grass. Call this out as a site safety issue, not a housekeeping issue. · Some students will treat the spirit level as a scraper, a lever or a hammer during clean-up. Reinforce that a level dropped or used as a pry bar is now scrap - check it for straightness against a known straight edge and reverse-read the vial before it goes back on the rack. · Expect confusion about controlled waste. Have the site waste plan and the SDS for the marking paint on the table and make students find the answer in the document rather than asking you. · Students working in pairs often both assume the other one did the equipment register. Assign the paperwork to a named person in the team brief and check it at handover. · Time the clean-up. On a real job it is done under pressure at the end of the day, and a student who can only do it properly with unlimited time has not met the standard. · Link back to Element 1 - the SWMS or JSA for the levelling task usually has clean-up as its last step, including the waste and housekeeping controls. Ask students to point to it.

## Slide 46
CPCCCM2006 · Element 3 — what you need (1/3)
What you need (1/3)
Element 3 — Clean up
Automatic or optical level with its manufacturer's manual and padded carry case
Aluminium tripod with adjustable legs, wing nuts and rubber or spiked shoes
5 m telescopic levelling staff with a staff bubble
Rotating laser level with detector, staff clamp and remote
1200 mm box spirit level and 1.8 m aluminium straight edge
Water level hose and fittings, and a bucket for draining
Claw hammer and star picket puller

## Slide 47
CPCCCM2006 · Element 3 — what you need (2/3)
What you need (2/3)
Element 3 — Clean up
Hi-vis peg caps, marking paint and witness pegs
Line winder and spare stringline
Lens brush or air blower, and a clean microfibre lens cloth
Clean lint-free rags, a spray bottle of clean water and a soft brush
Broom, shovel, wheelbarrow and rubbish bucket
Site waste management plan and bin signage for timber, metal, plastic, concrete and general waste
Controlled waste container for used batteries and empty aerosols
SDS for the marking paint in use

## Slide 48
CPCCCM2006 · Element 3 — what you need (3/3)
What you need (3/3)
Element 3 — Clean up
Out-of-service tags and the organisation's fault report form
Equipment and calibration register, and the job level book or field sheet
Hard hat, hi-vis clothing, steel-capped boots, safety glasses, cut-resistant gloves
P2 disposable respirator for dry sweeping of dust and dried slurry
Sunscreen and drinking water for outdoor work

## Slide 49
CPCCCM2006 · Element 3 — 1. Element 3 - Clean up: what it covers
Element 3 - Clean up: what it covers
Element 3 — Clean up
Clear the area you worked in, sort what you generated
Dispose or recycle to statutory and authority requirements
Clean, check, maintain and store every tool used
Manufacturer specification decides how gear is stored
Last step in the SWMS, not an optional extra
Notes: Clean up is the last part of every levelling job, and on a construction site it is the part that most often gets rushed. When the last height has been marked, the area you worked in still holds string lines, redundant pegs, offcuts, spent marking paint cans, flat batteries and the mud you tracked around while shooting levels. Your instrument, staff, tripod and spirit level are all sitting where you left them, usually dirty and often damp. The element asks for two things: the work area is left clear, with everything you generated sorted into the right waste stream or set aside for re-use, and the tools and equipment go back into store clean, checked and set up the way the manufacturer says to store them. It matters for three reasons. First, safety and site liability: a pulled peg leaves a hole, an uncapped star picket left standing is an impalement hazard, and a coil of string line across a walkway is a trip. Second, cost and compliance: mixed waste in the wrong bin costs the builder money in sorting fees, and batteries, aerosols and contaminated water are controlled waste that the EPA in your state and the local council will not let you put in the general bin or wash into a stormwater pit. Third, accuracy: a levelling device is a measuring instrument, not a hand tool. Grit on the tripod head, mud caked on the foot of a staff, a lens wiped with a dirty shirt, or an instrument cased wet will all cost you accuracy on the next job or send the instrument out for repair. Doing it properly follows a set order. Before you touch anything, find out what has to stay - the datum peg, any transferred heights still in use, and profiles the next trade is working from. Then clear only what is finished with, sort as you pick up rather than making one big pile to deal with later, and dispose of each stream where the site waste plan says it goes. Clean the gear from the outside in: body and legs first with a damp rag, then optics last with a proper lens brush and lens cloth, never solvent and never your sleeve. Check as you clean - cracked vial, bent staff section, chewed tripod thread, loose clamp - because cleaning is when you are actually looking at the equipment. Anything faulty gets tagged out and reported, not put quietly back on the shelf. Then case it, lock or clamp the instrument the way the manual specifies, store it dry and off the ground, complete the equipment record, and tell the supervisor the area is clear.

## Slide 50
CPCCCM2006 · Element 3 — 2. Before you pull anything out
Before you pull anything out
Element 3 — Clean up
Ask the supervisor what stays - datum, profiles, live marks
Record datum location and RL in the level book
Cap or flag retained pegs so a machine operator sees them
Unknown peg? Leave it standing and report it
Lost datum means the whole set-out is re-run

## Slide 51
CPCCCM2006 · Element 3 — 3. Clearing the area
Clearing the area
Element 3 — Clean up
Coil string line onto a winder - do not bin re-usable line
Pull redundant pegs and pickets, backfill every hole
Cap or pull star pickets - impalement hazard
Sort into a bucket as you pick up, never one big pile
Damp down and wear P2 before dry sweeping slurry

## Slide 52
CPCCCM2006 · Element 3 — 4. Waste streams on a levelling job
Waste streams on a levelling job
Element 3 — Clean up
Timber, metal, plastic, concrete, general - read the bin sign
Flat batteries and aerosols are controlled waste
Never puncture, crush or burn an aerosol can
Water level water goes to wash-out, never a stormwater grate
Sound pegs and profile timber stacked off the ground for re-use

## Slide 53
CPCCCM2006 · Element 3 — 5. Cleaning order - outside in
Cleaning order - outside in
Element 3 — Clean up
Body, tripod legs and staff first with a damp rag
Clean the staff foot - 2 mm of mud is 2 mm of error
Optics last: blow or brush, then lens cloth only
No solvent, no sleeve, no paper towel on coated glass
Dry everything before it goes anywhere near the case

## Slide 54
CPCCCM2006 · Element 3 — 6. Cleaning is your inspection
Cleaning is your inspection
Element 3 — Clean up
Bubble vial - cracked housing or split bubble
Staff - bent sections, worn clamps, unreadable face
Tripod - loose wing nuts, worn shoes, grit in leg clamps
Laser - chipped window, corroded battery contacts
Fault found = out-of-service tag plus fault report today

## Slide 55
CPCCCM2006 · Element 3 — 7. Storage that protects the instrument
Storage that protects the instrument
Element 3 — Clean up
Set transport lock or compensator clamp per the manual
Seat in the case foam - if you are forcing it, it is wrong way round
Remove batteries from laser, detector and remote
Store dry, off the ground, away from heat and vibration
Update the equipment record and next two peg test due date

## Slide 56
CPCCCM2006 · Element 3 — 8. What good looks like at handover
What good looks like at handover
Element 3 — Clean up
Only intended pegs standing, capped and visible
No holes, no loose line, no offcuts, clean access ways
Bins uncontaminated, controlled waste in its container
Gear clean, dry, cased, locked away, records complete
Verbal handover: what stays, where the datum is, what is tagged

## Slide 57
CPCCCM2006 · Performance criterion 3.1
3.1
Work area is cleared and materials sorted and removed or recycled according to statutory and regulatory authority requirements.

## Slide 58
CPCCCM2006 · Performance criterion 3.2
3.2
Tools and equipment are cleaned, checked, maintained and stored according to manufacturer specifications.

## Slide 59
CPCCCM2006 · Element 3 — activities (1/4)
Activities (1/4)
Element 3
Practical — Strip and clear a completed set-out area (60 min): Working in pairs on a set-out area you have already used for levelling, first confirm with your trainer or supervisor which pegs, profiles and marks must remain in place, and record the datum peg location and RL in your level book. Protect every retained peg with a hi-vis cap or witness peg. Then wind in redundant string lines, pull redundant pegs and pickets, backfill the holes, collect all offcuts, spent paint cans, batteries and packaging, and sweep or shovel spoil clear of walkways. Sort everything you pick up into the correct site waste stream as you go, and set re-usable pegs and profile timber aside on the stack. Finish by walking the area with your partner and pointing out any remaining trip, hole or impalement hazard, then hand the area back to your trainer.

## Slide 60
CPCCCM2006 · Element 3 — activities (2/4)
Activities (2/4)
Element 3
Practical — Clean, check, case and store levelling equipment (45 min): Using the automatic level, tripod, staff, spirit level and straight edge, and laser level you used on the job, carry out a full end-of-job clean and check with the manufacturer's manual open beside you. Wipe the instrument body, tripod legs and staff clean, paying attention to the foot of the staff and the tripod head, and dry everything before it goes near a case. Clean the optics with a lens brush and lens cloth only. Inspect each item as you clean it and note on the equipment record what you find - vial condition, staff clamp function, tripod wing nuts and shoes, straightness of the level, damage to the laser window. Remove batteries from the laser, detector and remote. Set the transport lock or compensator clamp as the manual specifies, seat the instrument correctly in…

## Slide 61
CPCCCM2006 · Element 3 — activities (3/4)
Activities (3/4)
Element 3
Written — Waste streams for a levelling job (30 min): You have just finished a day of transferring levels around a residential slab. In front of you is what you picked up: 14 broken hardwood pegs, six star pickets in good condition, about 30 m of used string line, two empty marking paint aerosols, four flat AA batteries out of the laser detector, a torn cardboard instrument carton, a bucket of water drained from the water level with cement fines in it, and half a bag of clean offcut timber. Using the site waste management plan and the SDS for the marking paint provided by your trainer, list each item, state which waste stream or destination it goes to, and state the reason - re-use, recycling, general waste or controlled waste. For the two items on the list that must not go into any bin on site, explain in a sentence each what would happen if…
Verbal — End-of-job handover to the supervisor (15 min): With your trainer acting as the site supervisor, give a two to three minute verbal handover at the end of a levelling job. Cover what has been cleared and what has deliberately been left standing and why, where the datum peg is and how it has been protected, where the recorded level results are, the condition of the equipment you used and anything you have tagged out, and any hazard you could not fix yourself and have reported. Your trainer will ask two follow-up questions.

## Slide 62
CPCCCM2006 · Element 3 — activities (4/4)
Activities (4/4)
Element 3
Quiz — Storage and maintenance quick check (20 min): Ten short scenario questions on end-of-job care of levelling equipment - casing a wet tripod, wiping a lens, storing a laser level over a two week shutdown, what to do with an automatic level that was knocked off the tripod, and where the manufacturer specification for storage is found. Closed book except for the equipment manuals, which you may use.

## Slide 63
CPCCCM2006 · Performance evidence (1/2)
Performance evidence (1/2)
What you must show to be assessed as competent
The person must also transfer levels and record differences in height for three different projects as required by job specifications, using at least three of the following levelling devices: a spirit level and straight edge, automatic/optical levelling device, levelling with water technique, laser levelling device.
conduct a two peg test with an automatic/optical level to confirm that the instrument meets manufacturer tolerances
locate, interpret and apply relevant information in job specifications to the levelling task
comply with site safety plan, and health and safety regulations applicable to workplace operations
comply with organisational policies and procedures, including quality requirements
safely and effectively use tools and equipment
communicate and work effectively and safely with others, including using agreed communication signals

## Slide 64
CPCCCM2006 · Performance evidence (2/2)
Performance evidence (2/2)
What you must show to be assessed as competent
confirm accuracy of the readings taken, including set-up and movement of device in two locations
accurately record results of each levelling procedure according to organisational requirements.

## Slide 65
CPCCCM2006 · Knowledge evidence
Knowledge evidence
What you must show to be assessed as competent
characteristics, technical capabilities and limitations of different types of levelling devices
methods of performing calculations associated with levelling
processes for setting out levelling tasks
requirements for line, level and plumb in construction projects
site and equipment safety requirements relevant to basic levelling procedures
symbols and construction terminology used when interpreting construction plans
techniques used when applying basic levelling procedures
contents of and terms used in job safety analyses (JSA) and safe work method statements (SWMS) and the use of this documentation when levelling.

## Slide 66
CPCCCM2006 · Assessment conditions (1/2)
Assessment conditions (1/2)
How and where this unit is assessed
Suitable assessment of performance requires:
equipment and tools:
as listed in the range of conditions and assessment requirements
specifications:
job requirements
health and safety requirements
manufacturer specifications
safety data sheets (SDS)
SWMS
workplace and relevant work site procedures
relationships with team members and supervisor:
work must be completed as part of a team and under direct supervision and observation

## Slide 67
CPCCCM2006 · Assessment conditions (2/2)
Assessment conditions (2/2)
How and where this unit is assessed
timeframe:
according to job requirements.
Assessor requirements As a minimum, assessors must satisfy the assessor requirements in the Standards for Registered Training Organisations (RTOs) current at the time of assessment.

## Slide 68
CPCCCM2006 · Sources and attribution
Sources
Sample RTO
CPCCCM2006 Apply basic levelling procedures is © Commonwealth of Australia, reproduced from training.gov.au under a Creative Commons Attribution-NoDerivatives licence. https://training.gov.au/training/details/CPCCCM2006
Learning content and assessment items in this document were drafted with AI assistance and must be reviewed by a qualified assessor before use with students.